## Slide 1
FENG 498
Backup Slides & Anticipated Questions
Defense backup for the jury. Mechanism deep-dive, sensitivity results, and 11 anticipated questions.
Section 1: Mechanism (3 slides) Section 2: Sensitivity (1 slide) Section 3: Anticipated Q&A (11 slides)
Schneider Electric Manisa | Supervisor: Dr. Oktay Karabag | IUE Industrial Engineering | June 2026

## Slide 2
01
Mechanism Deep-Dive
Backup section

## Slide 3
MECHANISM
How Line-aware Slotting actually works
Step 1: Per-line ABC. Rank each material by how often that production line consumes it, not by total demand.
Step 2: Kit co-location. Materials frequently picked together in a kit are placed in the same rack module or aisle.
Step 3: Manual-band placement. Each line's frequent items go to levels 1-3 nearest that line's kitting corridor, no reach truck needed.
Result: the operator picks a whole kit at hand height, near the line, without ever calling a reach truck.
Net effect: the RT queue never forms because the bottleneck resource is removed from the kit-pick path.
FENG 498 Backup

## Slide 4
MECHANISM
Why the queue collapses: the numbers
RT utilization drops: 21.7% to 1.3% (picking workload)
Operator wait drops: 8.45 min to 4.26 min
Kitting lead time drops: 12.37 min to 6.91 min, a 44% reduction
Throughput unchanged: approximately 398 orders/day across all policies
RT utilization and lead time correlate at r = 0.98 across the six policy means
Walk distance is flat: 89 to 109 m across all policies. The lever is the queue, not the aisle.
FENG 498 Backup

## Slide 5
MECHANISM
Live simulation demo
Show the live sim: switch to the 3D viewer, select 'Line-aware Slotting', follow Operator 1.
Narrate: picks stay on manual shelves at hand height, near the production line.
Count RT calls out loud: almost none under this policy.
Contrast with Travel-distance Optimized: same walk, but RT utilization 44% and lead time 24.6 min.
Key message: the absence of RT calls IS the entire effect, made visible.
Presenter note: open the sim_v2.html viewer. This slide replaces the live overlay during the presentation.
FENG 498 Backup

## Slide 6
02
Sensitivity & Stress Test
Backup section

## Slide 7
SENSITIVITY
The ranking is robust, and grows under load
OAT tornado analysis: Line-aware stays ranked first under +/- 20% variation on every input parameter.
Top sensitivity drivers: operator walk speed (approximately 40% of variance), arrival rate (approximately 39%), RT lift time (approximately 20%).
Stress test at 2x demand: the lead-time advantage widens from 6.2 min to 20.7 min.
Reason: under doubled load the baselines saturate the RT fleet while Line-aware is already near-RT-free.
Conclusion: the win is not a knife-edge. The policy is robust to uncertainty in input parameters.
See figures: sensitivity_tornado_avg_lead_time.png and stress_test_2x.png in the report figures folder.
FENG 498 Backup

## Slide 8
03
Anticipated Jury Questions
Backup section

## Slide 9
ANTICIPATED QUESTION
Why is the random seed the same across policies?
Answer:
Technique: Common Random Numbers (CRN). Seed = 42 + replication index.
Every policy faces the identical demand stream and service-time draws within a replication.
This isolates the policy effect: differences cannot be attributed to luck of the draw.
It makes the comparison paired, which lowers variance, tightens confidence intervals, and increases statistical power.
The seed varies across the 20 replications (42, 43, ..., 61) to capture real variability. Same seed within a replication keeps the comparison fair.
FENG 498 Backup

## Slide 10
ANTICIPATED QUESTION
Why simulation instead of a real pilot?
Answer:
Physical relocation of materials is costly and operationally disruptive at this scale.
Thousands of pallet positions would need to move before any result is observable.
Risk: disrupting live production in a high-volume MV switchgear plant.
Simulation gives every policy the identical demand stream: a fair comparison impossible in a sequential real trial.
Recommendation: use these results to design a small targeted pilot for the top-20 most impactful re-slots.
FENG 498 Backup

## Slide 11
ANTICIPATED QUESTION
Why this warehouse / company?
Answer:
Real industrial case: Schneider Electric Manisa, medium-voltage switchgear production.
High-volume operation: approximately 400 kit orders per day, 103 active working days analyzed.
Shared-resource environment: reach trucks, operators, Kardex carousels all compete. That is the interesting bottleneck.
Rich data access: SAP ZWM92 dispatch log (167,784 rows), material master (5,941 items), F400 video time study (2,319 micro-events).
Clear improvement potential: the research question is well-defined and answerable with the available data.
FENG 498 Backup

## Slide 12
ANTICIPATED QUESTION
Why these six policies, not just the proposed one?
Answer:
Baseline (Actual SAP): the real current operational practice. The benchmark all others must beat.
Capacity heuristic: a naive space-filling control. Tests whether any structure helps.
Usage-based ABC: single-criterion literature method, rank by pick frequency.
Double ABC: two-criterion literature method, cross-classify by cost and frequency.
Travel-distance Optimized: minimizes walking distance. Included to show distance is the wrong objective.
Line-aware Slotting (proposed): dependency-aware policy. The contribution.
Without the full field, the win could be dismissed as cherry-picking. Against all recognized alternatives, it stands.
FENG 498 Backup

## Slide 13
ANTICIPATED QUESTION
Are you optimizing the layout, or only the storage locations?
Answer:
We optimize storage-assignment decisions only. The physical layout is held fixed.
Fixed throughout: rack structure, aisles, resource fleet sizes, milk-run schedule, demand stream.
Optimized: which material goes to which location, manual-band vs reach-truck placement, line-based proximity, kit grouping.
No physical changes are required: zero new hardware, zero construction.
This is the key practical appeal: the improvement is a re-slotting decision, implementable without capital expenditure.
Scope: storage-assignment optimization within the existing building geometry and fleet.
FENG 498 Backup

## Slide 14
ANTICIPATED QUESTION
Double ABC is literature-based. Why did it not beat SAP?
Answer:
Double ABC sharpens priority classification, but still treats materials independently by aggregate demand.
It does not capture which production line consumes each item, or which items are co-picked in a kit.
Without line and kit dependencies, it cannot remove reach-truck calls from the kit-pick path.
Result: Double ABC increases RT utilization from 21.7% to 24.6% and lead time from 12.37 to 14.74 min (versus SAP).
Only the dependency-aware policy fixes the root mechanism. Classification quality alone is insufficient.
Comparison: SAP 12.37 min / 21.7% RT. Double ABC 14.74 min / 24.6% RT. Line-aware 6.91 min / 1.3% RT.
FENG 498 Backup

## Slide 15
ANTICIPATED QUESTION
If the goal is speed, why not just minimize walking distance?
Answer:
Minimizing distance parks the highest-frequency items in the closest rack positions, regardless of level.
Those closest positions are often on upper levels (level 4+), which require a reach truck.
Result: fast-movers flood the upper shelves, RT calls spike, RT utilization reaches 44%, and lead time hits 24.6 min, the worst performer.
Walk distance under Travel-distance Optimized is 96.1 m, only 7 m more than SAP at 89.0 m. Negligible difference.
Conclusion: in a high-bay shared-resource setting, cutting RT waiting time beats cutting walking distance.
Counter-intuitive finding: the policy that walks least has the highest lead time. Distance is the wrong objective.
FENG 498 Backup

## Slide 16
ANTICIPATED QUESTION
Is there enough manual-band capacity for all the fast-movers?
Answer:
The policy does not assume unlimited lower-level capacity.
It is a priority ordering: highest-frequency line items are placed first in the manual band (levels 1-3).
Next priority: co-picked kit items placed in the same aisle or rack module.
Then: shared multi-line materials placed in central accessible zones.
When the manual band fills, remaining lower-priority items spill upward, in priority order.
The benefit comes from getting the most impactful items into the best slots, not from infinite space.
Line-aware is a ranking rule, not a claim that every item fits in the ideal slot.
FENG 498 Backup

## Slide 17
ANTICIPATED QUESTION
Why is reach-truck utilization the key metric?
Answer:
Kit preparation time is dominated by waiting for a shared reach truck, not by the pick itself.
Operators arrive at the rack location and stand idle until a free RT is available.
The RT queue is the binding constraint. Walk distance barely varies across policies (89 to 109 m).
Cutting RT dependency, not walking distance, is the direct lever on lead time.
Line-aware drops RT utilization from 21.7% to 1.3% at stable throughput: all six policies deliver approximately 398 orders per day.
RT utilization and lead time correlate at r = 0.98 across the six policy means: strong empirical support.
FENG 498 Backup

## Slide 18
ANTICIPATED QUESTION
The chi-squared is significant. Doesn't that mean the model is wrong?
Answer:
No. The model uses its own routing logic, not a bin-for-bin replay of SAP history.
An exact chi-squared match would require replaying the historical dispatch sequence exactly, which defeats the purpose of a simulation study.
Read the effect size, not just the p-value. Cramer's V is approximately 0.24, which is small to moderate.
Chi-squared pooled statistic: chi-sq(7) = 535, using pooled cells to satisfy Cochran's rule (no expected cell below 5).
We label this an internal-consistency check, not out-of-sample validation. No independent holdout period was available.
Daily volume calibrated to within 1.1% of the real 396 kits per day. Route sanity: zero agents cross a rack body.
Significance at n = 5,900+ with our own routing is expected. Effect size Cramer's V = 0.24 is the honest read.
FENG 498 Backup

## Slide 19
ANTICIPATED QUESTION
Does the 1.27% RT figure hold in a live deployment?
Answer:
Not directly: the simulation scope is picking only.
Concentrating fast-movers on lower shelves increases replenishment frequency. Live total RT load will be higher.
The 1.27% (or 1.3%) reflects picking workload as measured in the model scope.
The relative ranking and lead-time advantage are preserved: replenishment load is identical across all six policies and not a differentiator.
Replenishment can be scheduled off-peak (overnight or shift changes), decoupling it from the kitting window.
Most important practitioner caveat: replenishment is out of scope but symmetric across policies. The lead-time win stands.
FENG 498 Backup