## Slide 1
Methodology & Simulation
Backup Q&A, anticipated jury questions
Deniz Ege Memetoglu | FENG 498 | Section 3
Plain backup sheet. Open in a second tab during Q&A. Numbers verified from the simulation output files.

## Slide 2
Q1. Is this a trace replay of the logs, or a real model?
Distribution-driven, not a replay.
• I fit distributions (inter-batch gap, batch size, kit composition, pick times) from 4 months of the ZWM92 dispatch log: 167,784 rows, 40,804 kit orders, 103 active days.
• The model SAMPLES from those distributions, it does not play history back.
• That is exactly what lets me move materials to new locations and re-run the SAME warehouse under a different policy. A replay could never test a new layout.
• Built in Python with SimPy (discrete-event simulation).
Deniz Ege | Methodology & Simulation | backup

## Slide 3
Q2. Why discrete-event simulation instead of a formula or a real pilot?
The bottleneck is queueing, which only DES captures.
• The delay is operators waiting for a shared reach-truck fleet, plus a cascade: an order holds its slot while it waits, delaying the next order.
• Static/analytic models assume average flow and miss this contention.
• A real pilot means physically moving pallets first; the simulation tests the policy at zero cost and zero risk, then we recommend a pilot as future work.
• Shared resources modelled: 8 operators, 7 reach trucks, 4 Kardex units, pallet-position locks.
Deniz Ege | Methodology & Simulation | backup

## Slide 4
Q3. Where do the pick / handling times come from?
From a video time-motion study of the F400 line.
• 2,319 micro-events, 296.6 observed minutes, coded from the F400 kitting video.
• Service times are lognormal with spread set by the measured CV: sigma = sqrt(ln(1 + CV^2)).
• Means: operator pick 0.113 min, reach-truck pick+place 0.110, manual penalty 0.102, Kardex pick 0.113.
• Sigmas: operator 1.245, reach-truck 1.047, manual 1.279 (moment-matched from the video CVs).
Deniz Ege | Methodology & Simulation | backup

## Slide 5
Q4. How did you validate the Kardex timing? There was no Kardex video.
Honest answer: it is an assumption, and it cannot bias the comparison.
• No Kardex-specific footage existed, so Kardex pick mean and CV MIRROR the F400 operator pick (0.113 min, sigma 1.245); carousel turn 0.4 min, sigma 0.30 (book value).
• This is disclosed openly in the report and assumptions.
• Kardex routing is identical across all six policies, so any timing error cancels out of the policy comparison; it shifts levels, not the ranking.
Deniz Ege | Methodology & Simulation | backup

## Slide 6
Q5. F400 timing is extrapolated to 9 product families. What if F400 is unrepresentative?
Sensitivity analysis bounds the risk; rankings are preserved.
• F400 is about 29% of dispatch rows; its timing is applied to the other 8 families.
• A one-at-a-time sensitivity sweep shifts every timing input by +/-20%.
• Line-aware Slotting stays the #1 policy under every swing; lead time moves proportionally, the conclusion does not flip.
• Per-line video time studies are listed as future work to retire this limitation.
Deniz Ege | Methodology & Simulation | backup

## Slide 7
Q6. Why model batch arrivals, and does the arrival rate match reality?
Because the real log arrives in batches, and the rate calibrates within ~1%.
• ZWM92 shows 3,885 same-timestamp batches, mean 4.68 kits per batch.
• Inter-batch gap mean 5.36 min with CV 2.04, so it is empirical, not Exponential.
• Analytic rate is about 419 orders/day; the full 20-replication runs measure ~398-400/day, within 1.1% of the real 396/day average.
• A single short 2-day check gave 378/day (-4.6%); all are inside the +/-10% band.
Deniz Ege | Methodology & Simulation | backup

## Slide 8
Q7. Why 20 replications, and why the same seeds across policies?
Common Random Numbers, and 20 runs separate the policies cleanly.
• Each policy runs N=20 replications; replication i uses seed 42+i, with separate streams for arrivals and service times.
• CRN means every policy faces the EXACT same demand, so differences are the policy, not luck.
• 6 policies x 20 = 120 runs (Minitab-ready).
• 95% confidence intervals (t, df=19) for Line-aware and the baselines are narrow and do NOT overlap, which is why 20 is enough.
Deniz Ege | Methodology & Simulation | backup

## Slide 9
Q8. Your chi-square is highly significant. Doesn't that mean the model is wrong?
No. Significance is expected here; read the effect size.
• Pooled chi^2(7) = 535.05, p < 0.001, but Cramer's V = 0.22 (small-to-moderate effect).
• It is significant because the model uses its OWN routing logic, not a bin-for-bin replay; an exact match would only happen if we replayed history, defeating the purpose.
• This is an internal-consistency check, not out-of-sample validation.
• Other checks: daily volume within 1.1%, and zero rack crossings in the 3D route audit.
Deniz Ege | Methodology & Simulation | backup

## Slide 10
Q9. You fitted and validated on the same ZWM92 data. No holdout?
Correct, and it is disclosed; no independent period was available.
• SAP never logged waiting times or reach-truck calls, so there was no separate observation period to hold out.
• Independent grounding still exists: the F400 video anchors the timing, daily volume calibrates to within 1.1%, and the 3D viewer confirms physically valid routes.
• We label these as internal-consistency tests, not a true holdout, on the limitations slide.
Deniz Ege | Methodology & Simulation | backup

## Slide 11
Q10. Aisle congestion is not modelled. Doesn't that invalidate the results?
It makes absolute times slightly optimistic, but the ranking is safe.
• Operators and trucks pass freely in shared corridors, so high-load lead times are a little optimistic.
• All six policies share this assumption symmetrically, so the comparison is fair.
• Adding congestion would only WIDEN Line-aware's lead, since the baselines saturate the reach-truck fleet far more (Travel-distance hits 44% RT utilization).
Deniz Ege | Methodology & Simulation | backup

## Slide 12
Q11. How real is the 'Actual SAP' baseline?
It is an honestly-labelled SAP-plus-heuristic hybrid.
• 750 materials sit at their exact decoded SAP rack-bay-position; 2,872 are Kardex-routed (policy-invariant); the rest fall to an FMR heuristic fallback.
• 386 materials have multiple SAP bins and are not split into forward vs reserve.
• We never claim a pure bin-for-bin replay; it is the best reconstruction the decoded SAP data allows, and it is the validation ground truth.
Deniz Ege | Methodology & Simulation | backup

## Slide 13
Q12. Throughput barely changes and RT utilization is only 1.3%. Is that believable?
Yes: the system is demand-limited, and 1.3% is picking-only.
• Every policy sees the same arrival stream, so throughput is ~398/day for all of them (ANOVA F about 0.01, p about 1.0). The win is in lead/wait, not output.
• RT utilization 1.3% reflects PICKING workload only; replenishment is excluded for ALL policies equally, so the comparison stays fair.
• In a live deployment total RT load would be higher once replenishment is added; this is the key caveat we disclose.
Deniz Ege | Methodology & Simulation | backup

## Slide 14
Q13. What about the milk-run trains?
Defined in the model, but operator-carried in the headline runs.
• The model represents 7 milk-run trains as an available transport mode.
• In the reported configuration the operator carries the finished kit to the line (milk-run delivery is switched off), so reported lead time is attributed to operator and reach-truck only.
• This is a modelling choice, disclosed; enabling milk-run would offload operator walking, it does not change the reach-truck queue that drives the result.
Deniz Ege | Methodology & Simulation | backup

## Slide 15
Q14. Is the warehouse layout real or invented?
Reconstructed from the real AutoCAD drawing and rack PDFs.
• Geometry from the AutoCAD DWG plus 11 per-rack pallet PDFs, cross-checked by a blind CAD extraction.
• 11 rack rows (A-J and U); 3,101 modelled pallet positions reconcile with the 3,203 drawing capacity (the 102 gap = narrower feeder bays plus a cart-parking slot).
• 5,941 active materials processed; this is a faithful digital twin of the floor.
Deniz Ege | Methodology & Simulation | backup

## Slide 16
One-glance numbers (Line-aware vs SAP baseline, N=20 CRN)
KPI | Line-aware | SAP baseline | Change
Lead time | 6.91 min [6.44, 7.38] | 12.37 min | -44%
Operator waiting | 4.26 min | 8.45 min | -50%
Reach-truck utilization | 1.27% | 21.71% | -20.4 pts
Operator utilization | 27.5% | 40.5% | lower
Walking distance | 92.4 m | 89.0 m | +3.8%
Throughput | 398.6 / day | 398.5 / day | unchanged
Effect size: Cohen's d = 3.10. Paired-t vs SAP: t about -17.5, p about 3.7e-13.
ANOVA: lead F=47.07 (eta^2=0.67), RT util F=430 (eta^2=0.95), throughput F about 0.01 (no effect).